#332 – Structure Fire - Rural

Date Issued: 10/06/2006

Date Last Revised: 10/06/2006

Purpose and Scope:

To establish guidance for fighting rural structure fires. This guideline applies to all members of the department.

Guideline:

All personnel shall observe the practices and precautions established in this guideline when responding to rural structure fires. The incident commander may adapt and modify the guideline as required by the magnitude of the emergency and existing conditions.

Procedure:

General

Fire fighter/first responder safety and health shall be the overriding consideration at all emergency response operations and shall take priority over all other factors.

All personnel shall check in and out by the established Passport Accountability System.

All fire fighters shall wear NFPA compliant protective clothing consisting of:

Protective coat

Protective pants

Helmet with goggles

Boots

Gloves

Fire retardant (NOMEX) hood

Personnel exposed to vehicular traffic shall wear reflective vests.

Self-contained breathing apparatus (SCBA) with PASS alarm shall be worn by fire fighters operating in, adjacent to or above active fire areas.

Fire fighters shall operate in pairs.

A two person backup team wearing full protective equipment including SCBAs with pass alarms shall be provided when fire fighters operate in, adjacent to or above active fire areas.

The backup team shall have a charged attack line.

The backup team shall provide hoseline protection as required.

Medical personnel shall be on ready standby when fire fighters operate in, adjacent to or above active fire areas.

Fire fighters shall use care and caution when entering burning structures.

Stand off to side when opening doors/windows. Limit damage to structure when forcing entry.

All fire fighters shall maintain a clear means of escape when entering active fire areas.

Personnel shall remain alert for fire ground safety and health hazards:

- Overhead power lines

#332 – Structure Fire - Rural

Date Issued: 10/06/2006

Date Last Revised: 10/06/2006

- Vehicular traffic

- Hazardous materials

- Backdraft and flashover conditions

- Structural failure—steel truss roofs, overhangs and false fronts

- Any condition that does not look or feel right

All hazards shall be reported to the IC/ Safety Officer.

All personnel shall take adequate rest periods and remain alert for any signs/symptoms of heat stress or hypothermia/frostbite.

Personnel with signs or symptoms of heat stress or hypothermia/frostbite shall report to the rehab area (if a rehab area has not been established report to the IC/ Safety Officer).

Personnel shall report all injuries and/or symptoms of illness to the IC/ Safety Officer.

Action Plan

Resource Allocation

- Identify apparatus to be staffed (refer to SOG - Vehicle Response for Calls #201).

Communicate to dispatch (by radio) units responding and staffing

If adequate staffing is not available, request mutual aid by activation of the appropriate TEAMS box card and alarm level.

Approach

- En route to the emergency fire department vehicles shall be driven carefully at speeds that are appropriate for existing conditions.

Caution shall be exercised when approaching intersections and when traveling through residential areas.

All riders shall be seated with seat belts fastened.

While en route observe weather conditions and plan initial actions.

Approach from the uphill/upwind direction.

Approach scene with care and caution. Slow down and size up the situation as you approach. Be alert for special hazards:

  - Down power lines.

  - Involvement of hazardous materials (occupancy/location, container/vehicle type, markings/placards and/or unusual or unusual smoke/fire).

  - Other special hazards or circumstances.

Staging Fire Department Vehicles

Apparatus shall be staged at a safe location that is upwind of the fire. Location of Structure Fire

#332 – Structure Fire - Rural

Date Issued: 10/06/2006

Date Last Revised: 10/06/2006

#332 – Structure Fire - Rural

Date Issued: 10/06/2006

Date Last Revised: 10/06/2006

Incident Management

Actions Size-Up

- The ranking on-scene officer shall assume incident command and establish the incident management system.

Communicate to dispatch (by radio) command, units on-scene, staffing and situation. Advise dispatch of involvement and best approach.

Establish scene control and security.

Establish traffic control as required by the situation / location.

Request assistance from law enforcement as required.

Remove civilians to a safe location. As required assign fire fighter/medical personnel to comfort/console family/friends.

Have dispatch contact Red Cross if temporary housing or other assistance is required by the family.

If fully involved, increase the alarm level/ utilize the Tanker Task Force as required by the situation.

Fire Ground Operations

- Command shall review pre-incident plan if applicable.

- Command shall size-up the situation to identify priorities and tactics.

- Life/safety issues (is everyone out of the structure). Fire location, intensity and involvement.

- Entry points.

- Exposures.

- Weather conditions.

- Special hazards/conditions.

- Command shall identify and communicate priorities and tactics.

- Search and rescue.

- Offensive—interior fire attack and ventilation.

- Defensive—exterior fire attack and protect exposures.

- Identify priorities and tactics by life/safety issues, water supply and staffing.

- Secure Utilities

- Shut-off electric and gas services.

- Establish water supply (stage pumper).

- Position portable tank (position for ease of access by tankers).

- Connect draft lines to pumper.

- Discharge water from tanker into portable tank.

#332 – Structure Fire - Rural

Date Issued: 10/06/2006

Date Last Revised: 10/06/2006

- Tanker shall return to water supply for filling.

- Position any additional tanker(s) to discharge water into tank.

- Establish tanker shuttle.

Search and Rescue Operations

- As determined by existing conditions ventilate (forced or vertical) structure to reduce heavy smoke before entry is made.

- Search and rescue shall be performed by two person teams (buddy system) wearing full protective gear including SCBAs with pass alarms with a fully charged attack line.

- Chose rule of right or left and be consistent.

- Maintain contact with attack line.

- Perform primary search (fire area, floor above fire and fire floor) and secondary search (other areas or structure).

- Identify rooms/areas that have been searched.

Interior Fire Attack

- As determined by existing conditions ventilate (forced or vertical) structure to reduce heavy smoke before entry is made

- Interior fire attack shall be performed by two person teams (buddy system) wearing full protective gear including SCBAs with pass alarms.

- Attack fire by suitable means—attack line or fire extinguisher.

- Coordinate attack teams.

- Minimize property damage. When possible remove or cover furnishings.

- Maintain contact with attack line.

Exterior Fire Attack/Exposure Protection

- Exterior fire attack shall be performed by two person teams (buddy system) wearing full protective gear including SCBAs with pass alarms.

Based on existing conditions SCBAs may be omitted at the discretion of the safety officer.

Coordinate attack teams.

Vertical Ventilation

- Coordinate ventilation with other fire ground operations.

Fire fighters operating on roofs that are directly above active fires shall operate in pairs and wear full protective equipment including SCBAs with pass alarms.

Place two ladders for alternate means of escape.

#332 – Structure Fire - Rural

Date Issued: 10/06/2006

Date Last Revised: 10/06/2006

Place roof ladder on roof. Fire fighters shall remain on the roof ladder.

Cut ventilation hole at the desired location using suitable tools.

Forced Ventilation

- Coordinate ventilation with other fire ground operations.

Fire fighters positioning forced ventilation equipment shall operate in pairs and wear full protective equipment including SCBAs with pass alarms.

Place mechanical ventilator.

Provide a second opening in structure to ventilate desired room/area.

Salvage and Overhaul

- Salvage and overhaul shall be performed by two person teams (buddy system) wearing full protective gear including SCBAs with pass alarms.

Based on existing conditions SCBAs may be omitted at the discretion of the safety officer.

Protect structure/contents from unnecessary damage.

Locate and extinguish all hot spots.

Place structure in a safe condition.

Incident Termination

- Determine fire origin and cause.

- Preserve any evidence if arson is suspected. Notify law enforcement and State Fire Marshall.

- Return control of structure to owner/tenant.

- Be sure the fire is completely extinguished before returning to station.

- Insure that all fire fighters are accounted for before leaving scene.

- Communicate to dispatch (by radio) that the incident has been terminated and that all units are returning to station.

- Clean apparatus and equipment.

- Replace used or damaged equipment on apparatus.

- Fuel apparatus.

- Conduct a debriefing as required for the incident.

- Note any signs of stress, injuries or complaints of illness. Ensure follow-up.

- Complete incident reports.

# Text boxes

332a

Example of Staging at a Rural Structure Fire (Not to Scale)

Personnel Staging

& Rehab

Incident

Command

Staging

Officer

Wind Direction

Pumper

Tanker

Tank

Tanker

Direction of Travel, Leaving

Direction of Travel, Arriving

Safety

Officer

332b

332c

332d

332e

332f